## Slide 1
CMP3103M Autonomous Mobile Robotics -Assessment Item 1
By Daniel Dixon 16602092

## Slide 2
Design and Implementation
Imported/Subscribed
  Image – Used to create masks
  Scan – Used to calculate distance
  Move_base – Used to create a client
Exported/Published
  Debug – String Publisher that states which poles have been found
  Mobile_base – Data published to here for movement
Other topics shown would have been used for further inmplimentation

## Slide 3
Evaluation
Limitations of code:
  Map – Although attempts at implementation, code is not resilient to changes in the map
  Object Avoidance – If object to be found is at a certain point where enough is showing but an object is in the way it will bang into that object
  Move_base Integration with Twist Movement - The twist movement that takes place when moving towards the poles can cause the mapping to need a reset by move_base. To combat this an implementation that calculated the distance away from the object and then recursively computed a move_base goal closer and closer to the object until the turtlebot was less than a metre away
Results:
  All four objects found
  Time Taken without poles: (mm:ss:msms)03:30:69
  Time Taken with poles: (mm:ss:msms)03:06:45
  Taken less time with poles as all poles found before route completed
Improving efficiency:
  Visit less locations
  Don’t have robot turning to initial orientation at each location
  Spin at each location combined with smaller minimum mask area